## Slide 1: FlexGate: High-performance Heterogeneous Gateway in Data Centers
Kun Qian, Sai Ma, Mao Miao, Jianyuan Lu, Tong Zhang,
Peilong Wang, Chenghao Sun, Fengyuan Ren
Notes: Hello everyone. I am Kun Qian from Tsinghua University.
Today I will talk about FlexGate: High-performance Heterogeneous Gateway in Data Centers

## Slide 2
E6636BC20180234D78A0072836F0BB10F2B9B2051A920BB0A1D98E30B1042B29EB4CB038E16D3B0D22592108384626EBFA19217A11D0BB011BBFC2167A0E1BD124FE97ADDC216457C4072FF76F5245B389FCE1CE77D812D49806D19FEA190C68DA862A91FE3
E6636BC20180234D78A0072836F0BA20C2B9B20112BE5BF0A4D98E3CB15E2BF92B41B838E1663B0E22992008384676EB021921FA31D00B711BBFC2637E1E1DDA24FE20ADB323748714E024876FB245C688B6E2CA770772A298961193354FBC78DDD62F90CE3
E6636BC20180234D78A0072836F0B1C0E2B9B20B12B38B80ADD98E33B13E2B29EB46B838E16B3B092239200838468BEB8A1921AA31D0DB911BBFC2187D2E1DD524FE91AD112384B734BD2D676FF245C6EE22ECCE770D128698F6A19A110FBCA8DCD629942E3
19
110+
1500+
Regions
Access points
Edge points
Northern China
E6636BC20180234D78A0072836F0BE9092B9B2041933FB20A3D98C34B1982BF66B44BC38E16C8B0722E92508384636EB4A19218AB1D0EB911BBFC21572BE16D324FE96AD1F2CA4F784F92EB7616245511A40E9EA72A07113F8BF919778145C48D9A620910E3
E6636BC20180234D78A0072836F0BC50A2B9B20E179E3B50A3D98B31B15E2BA67B44B738616CFB0422592308384662EBB519215A11D0FB511BBFC2247FAE1BD724F9B7AD002374E7B4172BF768624ED33744EEE5760761E368BB419EEF394C18DF8625926E3
Cloud Data Centers
Southern China
Hong Kong
Hang Zhou
Shang Hai
US West
US East
Britain
Germany
Middle East
India
Singapore
Malaysia
Indonesia
Japan
Australia
Notes: Alibaba has deploy many data centers around the world to support various applications for people in different area.
As shown in the Figure. There are 19 main regions, more than 100 access points and one thousand five hundred of edge points to access the service in the cloud.

## Slide 3
Data Center Gateway
Data center gateway needs to support:
  Various functions
  NAT, VxLAN encap./decap.
  ACL
  Monitoring, Metering, QoS mapping
Notes: In each data center, there is a gateway on the boundary to process every packet on both direction[click].
It needs to support various functions, including fundamental ones like NAT, VxLAN encapsulation and decapsulation.
Furthermore, to improve the performance and security, operators prefer to deploy customized network functions on the boundary.
For example, ACL is deployed to block unqualified traffic.
Monitoring, metering and QoS mapping are used to provide necessary guard for performance.

## Slide 4
Data Center Gateway
Data center gateway needs to support:
  Various functions
  High throughput
Notes: Nowadays, data centers support many widely used network applications, which serve gigantic traffic from huge amount of clients.
We measure the inbound/outbound throughput around 4 operating data centers in one week.
The values of throughput vary from hundreds to thousands of gigabits per second.
When encountering special events (like shopping festival), the load-bearing throughput would be further higher.

## Slide 5
Data Center Gateway
Data center gateway needs to support:
  Various functions
  High throughput
  Large number of flows
Notes: High throughput also means that the number of flows served by the data center is large.
We further record the total flow numbers (distinguished by 5-tuples).
Each data center serves millions of different flows.
With the increase of number of flows, the number of matching rules in each gateway function increases at the same time.
Considering that some gateway functions execute matching at the flow level, storing millions of rules puts forward severe challenges on both storing and efficient accessing.

## Slide 6
Software Gateway Cluster
Supporting traffic at terabits per second needs dozens of servers.
  High expenditure
  Hard for operation and maintenance
Notes: In the last decade, NFV is proposed to implement functions on inexpensive, commodity processors.
It provides advanced processing and storage ability.
Furthermore, software-based solution greatly simplifies the procedures of creating new functions and updating old ones.
However, advanced NFV platforms can only support the execution of network functions at ten to forty Gbps.
For processing terabits per second of traffic, dozens or even hundreds of servers need to be deployed.
Deploying software gateways at this scale not only is expensive but also causes great burden and challenges for operation and maintenance.

## Slide 7
Programmable Hardware
Supporting flexible packet processing at up to 6.5Tbps.
Limited processing and storage resources:
  Up to 12/32 match-action stages in each pipeline.
  Each physical stage contains up to 1.5MB SRAM and 160KB TCAM.
Notes: Emerging programmable packet processing hardwares can support flexible packet processing at ultra-high line rate, which offers a new option for implementing gateway functions.
When a new packet arrives, [click] firstly a parser extracts packet headers according to the user-defined parse graph.
Then [click] the packet goes through the ingress and egress pipeline.
To support flexible per-packet processing, each pipeline is composed of many match-action stages.
A network function would be implemented by combining a series of stages in hardware.
Although these programmable hardwares provide satisfying flexibility and throughput, they have two intrinsic drawbacks.
Firstly, constrained by the chip area, programmable hardwares contain limited number of stages.
Second, each physical stage contains limited storage resources.

## Slide 8
Heterogeneous Gateway
Software gateway and programmable hardware are complementary.
Notes: Software network function platform and programmable hardware are complementary.
This slide gives a detailed summary of the pros and cons of deploying software gateway and programmable hardware.
Specifically, software gateway possesses flexible processing and huge storage while providing limited throughput, and programmable hardware has opposite features.
It inspires us to propose the hardware-software co-design gateway to meet all requirements.

## Slide 9
Observation
1. Functions serve different proportions of traffic
Fundamental functions services (e.g., VxLAN encap./decap.) match all incoming traffic.
Widely-used functions (e.g., IP NAT) handle a large percentage of traffic (~99%).
Some functions only serve small portions of traffic.
Port NAT and SNAT serve 0.11% and 0.83% of traffic respectively.
Notes: We have two observations which help us to design the heterogeneous gateway.
The first observation is gateway functions serve different proportions of traffic.
We monitor gateway in 4 different operating data centers and record the percentage of traffic processed by each network function.
Results show that the proportion of traffic served by different functions varies greatly.
Some functions process almost all flows.
Intuitively, fundamental functions (like VxLAN encapsulation decapcapsulation) match all incoming traffic.
Other widely-used functions (e.g., IP NAT) handle a large percentage of traffic.
On the other hand, other functions only serve small portions of traffic.

## Slide 10
Observation
2. Pareto principle in rule matching
In each function, different rules serve different percentage of traffic.
5% of rules serve more than 90% of traffic.
Notes: The second observation is Pareto principle exists in rule matching.
In each function, different rules serve different percentage of traffic as well.
We record the rule matching times of IP NAT in one hour as an example.
Rules are sorted by their matching times from high to low.
Results show that small portions of rules match most part of traffic.
In IP NAT, 5 percent of rules serve more than 90 percent of traffic, while the resting rules are matched in infrequent conditions.
Through observations, this principle also suits most functions employed in gateway.

## Slide 11
Basic idea
1. Functions serve different proportions of traffic.
2. Pareto principle in rule matching.
Arranging frequently-used functions in hardware
Placing hot rules in hardware
Notes: The basic idea of FlexGate is simple: fully utilizing programmable hardware to process the vast majority of traffic and leveraging software gateway to deal with the residual.
Based on the first observation
We give the first principle:…
Based on the second observation
We give another principle:…

## Slide 12
FlexGate
Notes: We take four functions as an example to introduce the processing procedure in FlexGate.
As shown in the figure, [click] the software possesses the entire function pipeline, which can process any traffic.
[click][click] Function one, two and four are offloaded to programmable hardware and only partial matching rules of function one and two are stored in hardware.
Incoming traffic first enters into programmable hardware.
Most packets are completely processed and propagated by hardware.
[click][click] Due to incomplete match table, function one and function two may miss some packets and they will be redirected to software for further processing.
Similarly, [click][click] packets requiring the processing of function three will also be transferred to software.
In our design, once a packet enters into software, it will stay in software until all subsequent executions are finished.
We make this design decision mainly for decreasing software-hardware transfer.

## Slide 13
FlexGate
Notes: This figure illustrates the deployment of FlexGate.
As a whole, FlexGate links to the border router in a hanging way.
To provide better scalability, [click] packets are transmitted from hardware platform to software platform through network.
So both hardware and software platforms can deploy flexible system extension. [click disappear]
Considering the scale of unmanageable traffic may be very large.
It is impossible for a single server to process such large throughput. So we build a small software cluster to execute software processings.

## Slide 14
Pipeline Load Balance
Load balancer in ingress pipeline.
All functions are implemented in the egress pipeline.
Notes: Actually, up-to-date programmable hardwares have multiple pipelines.
Different pipelines possess independent match-action stages and storage resources.
In order to fully utilize them, We only implement [click] the header parser and pipeline load balance modules in ingress pipelines, and all network functions are deployed in egress pipelines.
This architecture enables flexible load balancing.

## Slide 15
Pipeline Load Balance
How to balance load to different pipelines?
Round-robin load balance?
Semantic inconsistency
5-tuple load balance?
Waste storage resource
Notes: The following key issue is finding appropriate criteria to split matching tables to different egress pipelines.
The most straightforward method is splitting packets in a round robin way.
[click] However, with this way, packets from the same flow may be processed by different pipelines, which may introduce semantic defect.
For example, flow state monitors run on different pipelines may deduce different states for the same flow.
Another intuitive method is splitting traffic according to 5-tuple.
[click] It can keep the semantic consistency.
However, this splitting strategy would waste storage space.
Since most network functions match fields partially containing 5-tuple, packets matching the same rule of a function would be hashed to different pipelines.
So each pipeline needs to store completed tables for all gateway functions. It greatly wastes the precious storage resource.
The following slide gives an observation of the general gateway processings, which help us design the pipeline load balance

## Slide 16
eIP/vIP
Inbound
Outbound
Succeeding matchings are mostly based on eIP/vIP.
Notes: In data center, all inbound packets contain the elastic IP (eIP), which is the Internet IP exposed to tenants for serive accessing.
It needs to be mapped to the virtual IP ($vIP$), which is the corresponding VM IP inside the data center.
Then this field would be matched in subsequent network functions.
Similarly, in the outbound direction, $vIP$ will be mapped to $eIP$ and subsequent network functions would match it.
So splitting according to $eIP/vIP$ can efficiently divide matching tables into disjoint parts.

## Slide 17
eIP/vIP Load Balance
Inbound packets are hashed to different pipelines according to the destination IP field (eIP).
Outbound packets are hashed to different pipelines according to the source IP field in VxLAN header (vIP).
So workload is balanced and storage resource in all pipelines can be maximally utilized.
Notes: First, we identify the direction of a packet according to whether it has the VxLAN header.
If this packet comes from Internet, then it would be hashed to an egress pipeline according to its destination IP ($eIP$).
If this packet comes from the data center, then it would be hashed to an egress pipeline according to the source IP ($vIP$).
So workload is balanced and storage resource in all pipelines can be maximally utilized.

## Slide 18
Packet Transfer
Notes: During hardware processing, [click] unmanageable packets must be detected and transferred to software for entire processings.
[click] Limited by hardware restrictions, once a packet enters into the pipeline, it must go through the entire processing before being forwarded out.

## Slide 19
Packet Transfer
2
Notes: In order to guarantee the unchanged processing sequence and keep the semantic consistency, we add an extra field {operability} [click] in the packet header vector.
Once a packet is identified as unmanageable [click to red], its {operability} is set to false.
[click] Then all following functions do not deploy any modifications to this packet, and it will be transferred to software gateway to finish whole processing.
Furthermore, [click] in order to notify software gateway to start processing from which network function, we utilize the reserved field in VxLAN to record the next function id.
In the last stage of the egress pipeline, we implement a transfer load balancer to distribute unmanageable packets based on 5-tuple hashing.

## Slide 20
Scalability
Programmable hardware and software cluster are decoupled and exchange data through network.
So they can employ independent scale-up mechanisms.
Hardware:
Serial extension  Supporting complex functions.
Parallel extension  Supporting higher throughput.
Software:
Deploying more servers.
Notes: In FlexGate, programmable hardware and software cluster are decoupled. So they can employ independent scale-up mechanisms.
For programmable hardware, there are two modes for scalability.
When single programmable hardware cannot provide sufficient calculating and storing ability, we can employ multiple hardwares and organize them to work in pipeline.
On the other hand, if FlexGate needs to support higher bandwidth, we can deploy multiple ones in a parallel way and distribute incoming traffic evenly to them.
Furthermore, serial extension and parallel extension can be combined together to provide higher performance.
For software cluster, deploying more servers in the cluster can efficiently achieve linear scaling.

## Slide 21
Evaluation
Programmable hardware:
Tofino DFN-T10-032D
12 physical stages.
Each stage contains
1.28MB SRAM
67.6KB TCAM
1GHz clock
3.2Tbps throughput
Traffic:
Average throughput: 1.29Tbps
Peak throughput: 1.53Tbps
Software gateway cluster:
4 commodity servers.
32 2.5GHz cores.
256GB memory.
Notes: We employ Tofino as the programmable packet processing hardware. It has 2 independent pipelines. Each pipeline has 12 physical stages and each physical stage possesses 1.28 mega byte SRAM and 67.6 kilo byte TCAM. Tofino can provide totally 3.2Tbps throughput.
4 servers are deployed in the software cluster. Each server is equipped with 32 2.5GHz cores and 256GB memory.
We generate traffic according to the practical measurement and inject it to FlexGate. The average throughput is 1.29Tbps and the peak throughput is 1.53Tbps.

## Slide 22
Evaluation
Notes: 9 network functions are implemented in FlexGate and 7 of them are offloaded in programmable hardware. [click] Protocol processing and Port NAT/SNAT are only implemented in the software gateway. [click] The detailed resource consumption of each functions in one pipeline is presented in the table. As a whole, 85 percent of SRAM and 19 percent of TCAM in Tofino are consumed. In each function, rules most frequently matched in the history are selected to offload in the hardware.

## Slide 23
Evaluation
Pipeline load balance
Notes: we monitor the load of two egress pipelines to verify the performance of pipeline load balancer. Figure presents the average load of different pipelines.
Results show that $eIP/vIP$ load balancer may lead to at most $9.3\%$ of load imbalance.

## Slide 24
Evaluation
Transfer load balance
Notes: This figure presents the load of servers in the software cluster. In total, 8.6\% of traffic on average is transferred to software cluster for further processing. Furthermore, with the transfer load balancer, unmanageable packets are distributed evenly to all four software gateways.

## Slide 25
Evaluation
Overall latency
Notes: The overall processing latencies of FlexGate and software gateway clusters are shown in the figure. Most part of processing latency is around 1microsecond. The long tail of overall latency is caused by the processing of software gateways. With this heterogeneous architecture, the average latency of FlexGate is 1.28 microscond, and the 99% tail latency is 5 microsecond.

## Slide 26
Conclusion
FlexGate:
Programmable hardware + software cluster
1. Offloading widely-used functions in hardware.
2. Offloading hot rules in hardware.
eIP/vIP pipeline load balance to split workload.
Programmable hardware and software cluster can employ independent scale-up mechanisms.
Notes: FlexGate is a heterogenerous gateway by combining Programmable hardware and software cluster
It deploys two principles for implementing gateway functions:
(1)
(2)
In programmable hardware, eIP/vIP pipeline load balance is used to split workload.
Furthermore, programmable hardware and software cluster can employ independent scale-up mechanisms

## Slide 27
Thanks !

## Slide 28
Q & A