## Slide 1
Argus: Scalable and Deterministic Network Fault Localization for AI Training Clusters
Yuxiang Wang†, Jiao Zhang†∗, Xianyu Huang† , Yubo Ruan † ,Yuxuan Hu †, Yingjie Duan‡, Shoushou Ren‡, Xianjun He‡, Junlong Chen †, Yuan Li †, Tao Huang †
†State Key Laboratory of Networking and Switching Technology, BUPT, China
‡HUAWEI, China
1

## Slide 2
Outline
01
Background and Motivation
02
Design and Implementation
03
Evaluation
04
Conclusion
2

## Slide 3
The Era of Massive AI Training Clusters
01
Unprecedented Scale
Training of LLMs demands enormous computational power,with clusters utilizing massive parallel processing.
10,000+ GPUs
02
RDMA as Backbone
High-bandwidth,low-latency RDMA networks facilitate critical collective communication between nodes.
All-Reduce
All-to-All
03
Failure Impact
The "barrel effect" means a single faulty link can degrade the entire cluster's performance.
0.01% drops

## Slide 4
Limitations of Current Fault Localization Approaches
Current methods face significant challenges in AI training clusters,leaving critical gaps in reliability.
Switch-dependent
Require specialized hardware(e.g.,P4 switches),which is not always feasible in all clusters.
Infrastructure is costly and deployment across heterogeneous environments is challenging.
Passive Methods
Are reactive by nature and cannot proactively detect or predict issues before they occur.
Reliant on real-time data streams;lack of visibility into the health of idle or low-utilization paths.
Active Probing
e.g.,Pingmesh—Sends probes to measure network health,but has fundamental limitations.

## Slide 5
Motivations: Key Goals for Ideal Fault Localization
01
Achieving Deterministic Coverage
Current probabilistic probing (e.g., Pingmesh) leads to uneven coverage and blind spots. An ideal system must guarantee 100% deterministic link coverage to avoid missing faults.
02
Zero-Overhead Path Derivation
Path discovery methods like `traceroute` consume switch CPU and bandwidth. An ideal system should derive probe paths offline with zero network overhead.
03
Ensuring Fault Distinguishability
Concurrent failures often produce identical signatures with current methods. An ideal system must ensure unique fault signatures to accurately distinguish and localize multiple simultaneous failures.
5

## Slide 6
Outline
01
Background and Motivation
02
Design and Implementation
03
Evaluation
04
Conclusion

## Slide 7
System Overview of Argus
7
Offline Planner
Computes exact paths for candidate probes.
Selects a minimal set of probes for full coverage and distinguishability.
Outputs a “pinglist” to host agents.
Host Agents
Execute RDMA UD probes according to the pinglist.
Record outcomes and send lightweight reports.
Analyzer
Collects reports and performs fault localization using a tiered approach.

## Slide 8
Hash-aware Probe Planning
01
Deterministic Coverage Matrix
The planner replays the ECMP hash computation offline to build a matrix mapping probes to the links they traverse.
02
Probe Selection
Using ILP or a greedy algorithm, the planner selects a minimal set of probes to ensure 100% link coverage.
03
Edge Signatures
Probes are chosen to maximize the Hamming distance between link signatures,ensuring any two links can be distinguished.
8

## Slide 9
Tiered Diagnosis
Challenges
Hard Failures
Complete link outages that result in total service disruption.
Gray Failures
Subtle performance degradations,such as increased latency or low packet loss rates.
Design
1
Tier 1
Anomaly Detection
Flags probes with significant deviations from baselines to identify potential issues early.
2
Tier 2
Localization
Uses a suspicion-based algorithm to iteratively localize the exact source of hard failures.
3
Tier 3
Regression
Applies non-negative LASSO to correlate RTT deviations with per-link latency to quantify gray failures.
9

## Slide 10
Outline
01
Background and Motivation
02
Design and Implementation
03
Evaluation
04
Conclusion

## Slide 11
Probe Efficiency and Scalability
Distribution of probes per link
Total Probes for 100% coverage
Uniform Coverage
Argus achieves balanced coverage (1-3 probes/link),completely eliminating blind spots across all network links.
Probe Reduction
39x
fewer probes than R-Pingmesh for a 9,826-host cluster, while still achieving 100% coverage.
Argus achieves 100% coverage with unprecedented efficiency and scalability

## Slide 12
Planner Runtime
12mins
Plan the network for 9,826 hosts.
Greedy planners can efficiently handle large-scale clusters and are well-suited for dynamic environments where network topologies change frequently.
The greedy planner efficiently handles large clusters,taking only 12 minutes to plan for a 9,826-host network,making it suitable for dynamic environments.
12

## Slide 13
Evaluation:Localization Accuracy
Multi-link Failures
0.75-0.92
Maintains high F1 scores for 1-8 concurrent failures,far outperforming baselines.
Gray Failures(Delay)
0.67at 100µs delay
Successfully detects subtle latency increases,while baselines fail entirely.
Gray Failures(Loss)
0.005%-0.1%
Detects low packet loss rates,where baselines only detect higher rates.
13

## Slide 14
Runtime Overhead
The Argus agent is extremely lightweight,consuming minimal system resources.
CPU
1.0%
Average CPU utilization across all hosts
Memory
58MB
Average memory footprint per agent
This minimal overhead is achieved by offloading all complex computation to the offline planner and centralized analyzer.
This ensures that the agent remains a lightweight process on each host,without impacting the performance of production training workloads.

## Slide 15
Outline
01
Background and Motivation
02
Design and Implementation
03
Evaluation
04
Conclusion

## Slide 16
Conclusion
01
Unprecedented Efficiency
Achieves 100% link coverage with drastically fewer probes—39x less than R-Pingmesh.
Far more efficient than state-of-the-art while covering every network link.
02
High Accuracy
Effectively distinguishes and localizes both hard failures and gray failures.
Uses edge signatures and tiered diagnosis to pinpoint fault locations with precision.
03
Minimal Overhead
Operates with negligible impact on host resources.
Lightweight design makes it suitable for large-scale production environments without disrupting workloads.
16

## Slide 17
Thank You!
Contact Email
Wang_yx@bupt.edu.cn