## Slide 1: AI Data Center Networks: Traffic Characteristics, Technical Challenges, and System Optimization
Yang Xu
Fudan University

## Slide 2: Explosive Growth in LLM Scale and Inference Demand
Frontier LLMs are scaling rapidly, with training compute doubling roughly every 5–6 months.
LLM inference token volume continues to rise rapidly, while leadership among major models shifts frequently.
Evolution of LLM Scale [1]
One Year of the LLM Usage Race from Openrouter [2]
[1] https://huggingface.co/models，Models – Hugging Face
[2] https://openrouter.ai/models?order=top-weekly， Models – Top Weekly | OpenRouterModels
2
Notes: 把左图重画替换掉。具体要求见下一页

## Slide 3: A Common Blueprint for Large-Scale AI Fabrics : Multi-Tier, Multi-Plane, and Rail-Aware Connectivity
Meta, a three-level non-blocking topology
Alibaba, dual-plane multi-rail topology
OpenAI, multi-plane topology
[1] RDMA over Ethernet for Distributed AI Training at Meta Scale, SIGCOMM 2024
[2] Alibaba HPN: A Data Center Network for Large Language Model Training, SIGCOMM 2024
[3] https://openai.com/index/mrc-supercomputer-networking, 2026
3
Notes: 传统做法可能把一个 800Gb/s 网卡接口当作一个高速链路使用。MRC 的设计是把它拆成多个小链路，例如 8 个 100Gb/s 端口，连接到不同交换机，从而形成 8 个并行 network planes。这样可以用两层交换机连接约 131,000 个 GPU，而传统 800Gb/s 单平面网络可能需要三到四层交换机。相比传统三层或四层架构，这一设计显著降低了网络功耗与组件数量，在降低成本的同时提升了路径多样性。
自适应包喷洒技术
SRv6 源路由，微秒级绕过网络故障

## Slide 4
Training ：Hybrid Parallelism
M2N
Inference ：Disaggregated Serving
Take DeepSeek-V3 training as an example: PP, EP, and DP coexist
OSS/FS cluster
⋮
16-way PP, 64-way EP (across 8 nodes), 2-way DP
PD Separation + AF Separation
Q
Request
prefill node
MoE EP Parallel Traffic
attention node
FFN/expert node
GPU
GPU
GPU
GPU
PD Separation
AF Separation
Reply
$
KV Cache: stores intermediate state, avoids redundant computation, speeds up inference
Storage Layer
Get KV Cache
(Prefix)
Transfer
KV Cache
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
Why New AI Fabrics? AI Workloads Are Reshaping Network Traffic
decode node
Replica 1
(DP copy 1)
Stage 1
EP All-to-All
Stage 1
EP All-to-All
Stage 2
Stage 2
EP All-to-All
Stage 16
EP All-to-All
Stage 16
EP All-to-All
DP
sync
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
PP
comm
PP
comm
PP
comm
Replica 2
(DP copy 2)
PP
comm
PP
comm
PP
comm
…
…
PP Comm
EP Comm
DP Comm
Data Loading
KV Cache
M2N Traffic
EP All-to-All
4
Notes: Hybrid parallelism and disaggregated inference transform AI communication from generic any-to-any traffic into structured, synchronized, and topology-sensitive flows—driving multi-tier, multi-plane, and rail-aware fabrics.
左图：
把stage 3改成…，stage 4改成 Stage 16
把最小面一行的PP+EP…并行改成 16-way PP, 64-way EP（跨8节点），ZeRO-1 DP
把Stage 16和右边的箭头改成数据加载的
放了大概的参考图
右图：
把Attention节点与FFN/专家节点框起来，标上decode节点

## Slide 5: Feature 1: AI Traffic Demands Both Low Latency and High Bandwidth
3
Key Networking Technologies
•
Increase effective bandwidth
•
Reduce queuing delays
EP All-to-All-V Example
128 tokens
7168-dimensional vector
top-8 expert routing
Expert Parallel (EP) All-to-All-V
Expert 0
Expert 1
Expert 2
Expert 3
BF16
merge
Communication volume per layer = 22 MB
Time budget
TPOT = 20 ms
61 layers
Per layer ≈ 327 us
Comm budget ≈ 163 us
Network Time
8 * 200 Gbps = 1.6 Tbps network
Ideal comm time = 110 us
Jitter Budget
Only 53 us jitter budget
Even small bandwidth drops or queue build-ups exceed jitter budgets
1
Key Indicators of AI Traffic
Single-round comm task completion time
Communication completion time is jointly determined by data volume, effective bandwidth, and queuing delay.
2
Impact on performance
Training: A higher lengthens synchronization and reduces training throughput.
Inference: A higher worsens TTFT and TPOT and increases the risk of SLA violations
•
•
5

## Slide 6: Feature 2: AI Training Generates Periodic and Sync Traffic Bursts
1. Traffic has multi-level periodicity
Iteration-level: Data parallelism triggers gradient synchronization at each iteration.
Microbatch-level: At the microbatch level, pipeline parallelism repeatedly transfers activations and gradients.
Layer-level: At the layer level, tensor parallelism repeatedly performs collective communication within each Transformer layer.
★
Overlapping cycles produce structured, predictable bursts in link utilization.
4
Opportunity
Communication tempo makes traffic more predictable
Semantic-aware scheduling and communications priority
Resource allocation and bandwidth reservation
Challenge
Fine-grained irregular fluctuations
Short bursts can cause congestion
1
Data Parallelism (DP)
2
Pipeline Parallel (PP)
3
Tensor Parallelism (TP)
Hybrid Parallel (DP & PP & TP)
4
Periodic Link-Utilization Patterns Across Parallelism Strategies [1]
[1] CASSINI: Network-Aware Job Scheduling in Machine Learning Clusters, NSDI 2024
2. Opportunities and Challenges
6
Notes: Repeated compute–communication cycles synchronize thousands of GPUs, creating predictable yet intense traffic bursts.

## Slide 7
Feature 3: AI Fabrics Carry Heterogeneous Traffic with Conflicting Objectives
To avoid the cost of maintaining separate networks, the industry is converging AI and general-purpose traffic onto unified fabrics, as in ByteDance's Jakiro and Alibaba's Stella.
Challenges of Network Convergence：
(1) Competition for link resources between AI traffic and General-Purpose traffic
(2) Inference spans multiple communication stages whose traffic contends for shared links.
As AI traffic experiences more PFC pauses, flow completion time increases sharply.
Traffic from different inference requests overlaps in time and space, causing link congestion [1]
TCP flows coexist with RDMA flows
Link Contention Across Inference Stages
[1] Multi-stage Flow Scheduling for LLM Serving, arXiv 2026
7
Notes: These characteristics demand high-capacity fabrics, burst-aware congestion control, and strong performance isolation.

## Slide 8: Overview of Our Recent Work in AI Cluster Networking
GPU Cluster
Source
Traffic Generation
GPU Cluster
Spine layer
Leaf layer
Traffic Predict &
Engineering
Traffic Predict
Topology Reconfig
Switch's perspective
Ingress: isolation
Egress: schedule
GPU Cluster
Destination
Traffic Predict/ Engineering:
NetJIT [SIGMETRICS’25]
HalfLife (EuroSys’24]
Traffic Isolation:
InfiniFlow [SIGCOMM’26] /
Themis [NSDI'26]
Schedule:
BMW-Tree [SIGCOMM’23] /
vPIFO [SIGCOMM'24] /
Scale-up PIFO [SIGCOMM'26]
Traffic Engineer
8
Notes: 在这张图中进行以下修改：
将数据产生->预测与拓扑重构->这一条路径上的“入口隔离” 修改成流量隔离；将交换机视角内的”入口：隔离/Buffer管理”修改成入口：隔离
在最下面一行中，将每个工作的名字后面增加发表信息：NetJIT[SIGMETRICS’25]，InfiniFlow[SIGCOMM’26在投] Themis[NSDI’26]，AIRP[ToN’26], 3D-INA[INFOCOM’26], BMW-Tree[SIGCOMM’23],vPIFO[SIGCOMM’24]

## Slide 9
InfiniFlow:
Decoupling Virtual Channel Scalability from Buffer Requirements in Lossless Datacenter Networks SIGCOMM 2026

## Slide 10: Virtual Channels in Lossless DCNs
DCNs rely on hop-by-hop flow control to achieve lossless transmission.
  PFC in Ethernet
  CBFC in InfiniBand
Flow control mechanisms independently operate on each Virtual Channel (VC).
upstream switch
downstream switch
Q1
upstream port
downstream port
VC Buffers
B3
VC Queues
physical link
Q0
Q3
Q2
B2
B1
B0
Notes: 数据中心网络依赖hop-by-hop的flow control来实现无损传输
Flow control是以Virtual Channel为粒度工作的

## Slide 11: More VCs for Better Traffic Isolation
DCNs rely on hop-by-hop flow control to achieve lossless transmission.
  PFC in Ethernet
  CBFC in InfiniBand
Flow control mechanisms independently operate on each Virtual Channel (VC).
More VCs can enhance isolation between data flows, thus help to:
  mitigate Head-of-Line (HoL) blocking[1,2]
  prevent PFC/CBFC deadlock[2,3]
  enable finer-grained QoS scheduling[4]
[1] Kexin Liu et al. “Pyrrha: Congestion-Root-Based Flow Control to Eliminate Head-of-Line Blocking in Datacenter”. In NSDI 2025
[2] Prateesh Goyal et al. “Backpressure Flow Control”. In NSDI 2022
[3] Weihao Jiang et al. “Orderlock: A New Type of Deadlock and its Implications on High Performance Network Protocol Design”. In SIGCOMM 2025
[4] M.R. Siavash Katebzadeh et al. “Saba: Rethinking Datacenter Network Allocation from Application’s Perspective”. In EuroSys 2023.
Notes: 更多的VC有利于缓解无损网络中普遍存在的HoL阻塞和死锁问题，还可以实现更细粒度的QoS调度

## Slide 12: More VCs for Better Traffic Isolation
DCNs rely on hop-by-hop flow control to achieve lossless transmission.
  PFC in Ethernet
  CBFC in InfiniBand
Flow control mechanisms independently operate on each Virtual Channel (VC).
More VCs can enhance isolation between data flows, thus help to:
  mitigate Head-of-Line (HoL) blocking[1,2]
  prevent PFC/CBFC deadlock[2,3]
  enable finer-grained QoS scheduling[4]
[1] Kexin Liu et al. “Pyrrha: Congestion-Root-Based Flow Control to Eliminate Head-of-Line Blocking in Datacenter”. In NSDI 2025
[2] Prateesh Goyal et al. “Backpressure Flow Control”. In NSDI 2022
[3] Weihao Jiang et al. “Orderlock: A New Type of Deadlock and its Implications on High Performance Network Protocol Design”. In SIGCOMM 2025
[4] M.R. Siavash Katebzadeh et al. “Saba: Rethinking Datacenter Network Allocation from Application’s Perspective”. In EuroSys 2023.
What is the barrier to supporting more VCs?
Notes: 既然增加VC数量这么有用，那么为什么大家现在不这么做呢？

## Slide 13
The Barrier to Supporting More VCs
In CBFC, for each VC :
Lossless buffer quota for each VC
available buffer size
per-hop RTT
maximum achievable sending rate
per-hop BDP
Static allocation for lossless buffer
per-port buffer requirement
the number of VCs
Packet buffer space is the key barrier to supporting more VCs.
upstream switch
downstream switch
Q1
upstream port
downstream port
VC Queues
physical link
Q0
Q3
Q2
VC Buffers
B3
B2
B1
B0
Fixed quota for each VC
line-rate
13
Notes: 答案在packet buffer space
目前主流的flow control方法，为每个VC分配一块静态的VC buffer（click），这就导致了每端口的buffer总需求随VC数量线性增长
同时（Click），每个VC的buffer配额还不能太小，因为，为了保证无损传输，每个VC的最大传输速率与其buffer配额成正比
对于CBFC来说，VC的最大传输速率要小于buffer配额除以per-hop RTT
(Click)为了保证VC能以线速传输
（Click）每个VC的buffer配额至少要保证一个per-hop BDP
（Click）因此，在静态buffer分配下，每个端口所需的最小buffer space会随着VC数量快速增长
（Click）因此packet buffer是增加VC的关键瓶颈 【到这里用时2分钟】

## Slide 14
Inefficiency of Static Buffer Allocation
Scheduler
VCk
VCj
VCi
upstream egress port
downstream ingress port
VC queues
VC buffers
Buffer Manager
Occupied Buffer
Idle Buffer
Case 1 in CBFC: VCj is active alone.
Reserved Buffer for In-flight Packets
per-hop BDP
15 pkts
per-VC buffer quota is 5 packets.
…
…
…
…
14
Notes: 既然packet buffer如此precise，buffer有被充分利用好吗？
实际上，静态allocation下buffer的利用效率是很低的
我们看一个例子，在一段链路中，per-hop BDP假设是15 pkts，而由于总buffer不足而VC太多，（click）导致每个VC就分到了5 pkts的buffer space

## Slide 15
Inefficiency of Static Buffer Allocation
Scheduler
VCk
VCj
VCi
upstream egress port
downstream ingress port
VC queues
VC buffers
Buffer Manager
Occupied Buffer
Idle Buffer
Case 1 in CBFC: VCj is active alone.
Reserved Buffer for In-flight Packets
to egress port
per-hop BDP
15 pkts
wasted!
wasted!
per-VC buffer quota is 5 packets.
…
…
…
…
line-rate
15
Notes: 此时VC_j有流量到达，由于VC buffer太小，导致传输速率只有1/3线速（click）
想要提升速率需要更多的buffer，但是其他VC的buffer有不available to VC_j，(click)因此其他VC buffer就被wasted了

## Slide 16
Inefficiency of Static Buffer Allocation
Scheduler
VCk
VCj
VCi
upstream egress port
downstream ingress port
VC queues
VC buffers
Buffer Manager
Occupied Buffer
Idle Buffer
Case 1 in CBFC: VCj is active alone.
Reserved Buffer for In-flight Packets
to egress port
per-hop BDP
15 pkts
…
…
line-rate
line-rate
Shared buffer
16
Notes: 如果我们能将所有VC buffer聚合成一个shared buffer pool，（click）那么VC_j就可以获得足够的buffer，进而实现线速传输了

## Slide 17
Inefficiency of Static Buffer Allocation
Scheduler
VCk
VCj
VCi
upstream egress port
downstream ingress port
VC queues
Buffer Manager
Occupied Buffer
Idle Buffer
Case 1 in CBFC: VCj is active alone.
Reserved Buffer for In-flight Packets
to egress port
per-hop BDP
15 pkts
…
…
line-rate
Shared buffer
How large the shared buffer should be?
17
Notes: 如果我们能将所有VC buffer聚合成一个shared buffer pool，（click）那么VC_j就可以获得足够的buffer，进而实现线速传输了

## Slide 18
…
Scheduler
VCk
VCj
VCi
VC queues
…
Inefficiency of Static Buffer Allocation
Buffer Manager
Case 2 in CBFC: Three VCs are concurrently active.
line-rate
line-rate
line-rate
to port 1
to port 2
to port 3
upstream egress port
downstream ingress port
per-hop BDP
15 pkts
Shared buffer
line-rate
line-rate
Occupied Buffer
Idle Buffer
Reserved Buffer for In-flight Packets
18
Notes: 那么，这个shared buffer应该是多大呢，我们看第二个例子，假设三个VC同时传输流量，但是由于下游拥塞，（click）导致传输速率都只有1/3线速。此时，其实每个VC都不需要分配一整个per-hop BDP的buffer，而是只需要1/3 per-hop BDP的buffer，就可以使得聚合速率到达线速。

## Slide 19
…
Scheduler
VCk
VCj
VCi
VC queues
…
Inefficiency of Static Buffer Allocation
Buffer Manager
line-rate
line-rate
line-rate
Case 2 in CBFC: Three VCs are concurrently active.
to port 1
to port 2
to port 3
upstream egress port
downstream ingress port
per-hop BDP
15 pkts
Shared buffer
Key Insight
The aggregate VC rate is bounded by the physical bandwidth.
For a VC with rate ,
the buffer quota only needs to cover the in-flight data volume.
Theoretically, 1×per-hop-BDP of buffer space is sufficient.
line-rate
line-rate
19
Notes: 我们把这个结论泛化一下：（click）对于任意时刻，同端口所有VC的聚合速率受限于物理带宽。（click）如果我们可以给每个VC根据其传输速率分配恰到好处的buffer quota，那么理论上就可以把shared buffer具有1个per-hop BDP的空间大小就足以最大化链路利用率。

## Slide 20
…
Scheduler
VCk
VCj
VCi
VC queues
…
Design Goals of InfiniFlow
Buffer Manager
to port 1
to port 2
to port 3
upstream egress port
downstream ingress port
Shared buffer
Maximizing Link Utilization
2
3
Supporting more VCs with limited buffer capacity.
Lossless transmission
1
20
Notes: 基于这个key insight，我们提出了InfiniFlow。InfiniFlow的设计目标是，在保证无损传输（click）和链路带宽充分利用（click）的前提下，用limited buffer space支持大量的VC（click）
实现这三个目标的关键挑战的关键在于buffer在VC之间的划分
【到这里用时4分钟】

## Slide 21
Design Challenge & Solution
21

## Slide 22
Q1: Who Allocates the Buffer?
Traditional Local Allocation by Downstream Port
Scheduler
downstream switch
buffer allocation,
admission check
Buffer Manager
upstream switch
…
VCN-1
VC0
Scheduler
…
VC0
VCN-1
buffer allocation
Buffer Manager
1
The downstream manager decides how much buffer each VC gets.
2
The upstream scheduler knows how much buffer each VC needs.
separate from
22
Notes: 第一个问题是谁来分配buffer？通常，(click)交换机的buffer manager都是自己管理自己的buffer，（click）所以这种情况下，每一段链路的下游端口管理每个VC获得多少buffer。但是只有（click）上游端口才能知道每个VC需要多少。

## Slide 23
UABD in InfiniFlow enables immediate allocation for downstream buffer.
Immediate Buffer Allocation in InfiniFlow
Solution: Upstream Allocates Buffer for Downstream (UABD)
…
VCN-1
upstream switch
…
VC0
VCN-1
Scheduler
Scheduler
downstream switch
VC0
Immediate allocation
Immediate allocation
Credit pool serves as a proxy for the downstream shared buffer by tracking its overall availability.
1
Credit Pool
2
Scheduler not only allocates rates among VCs but also allocates buffer space based on the credit pool.
Upstream-Driven Buffer Allocation
buffer allocation for downstream VCs
23
Notes: 基于这个思路，我们提出UABD buffer管理architecture。首先，（click）我们在上游建立了一个credit pool作为下游shared buffer的代理，credit pool反映了下游buffer的当前总体可用量。基于这个credit pool，(click)scheduler不仅负责了速率分配，也负责了buffer space的分配。具体来说就是，每当scheduler调度一个VC，发送一个数据包，scheduler就会从credit pool中扣除指定大小的credit，（click）因此，UABD可以在保证无损传输的同时，实现buffer space的immediate分配

## Slide 24
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Shared buffer
Case 3: Two VCs are concurrently active without downstream congestion.
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
16 pkts
Idle Buffer
Occupied Buffer
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Reserved Buffer for In-flight Packets
24
Notes: 我们用一个例子更直观理解一下：初始状态下链路没有数据传输，shared buffer是空的。假设per-hop BDP是16个pkts，而shared buffer大小也正好是16 pkts，所以credit的初始值也是16 pkts。此时（click）有两个VC同时激活

## Slide 25
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
15 pkts
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
25
Notes: 调度器发送了一个yellow pkt，并且从credit pool（click）中扣除了对应volume。注意，This action相当于在下游shared buffer（click）中预留了对应volume的space

## Slide 26
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
14 pkts
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
26
Notes: 同样的，当调度器发送一个蓝色数据包的时候，那么蓝色VC相当于立即获得了对应volume的buffer space

## Slide 27
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
13 pkts
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
27
Notes: 接下来，round robin调度器就交替调度两个VC

## Slide 28
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
12 pkts
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
28
Notes: 接下来，round robin调度器就交替调度两个VC

## Slide 29
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
11 pkts
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
29
Notes: 接下来，round robin调度器就交替调度两个VC

## Slide 30
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
10 pkts
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
30
Notes: 接下来，round robin调度器就交替调度两个VC

## Slide 31
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
9 pkts
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
31
Notes: 接下来，round robin调度器就交替调度两个VC

## Slide 32
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
8 pkts
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
32
Notes: 接下来，round robin调度器就交替调度两个VC

## Slide 33
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
7 pkts
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
to port 1
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
33
Notes: 接下来，round robin调度器就交替调度两个VC

## Slide 34
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
6 pkts
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
to port 2
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
34
Notes: 接下来，round robin调度器就交替调度两个VC

## Slide 35
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
5 pkts
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
to port 1
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
35
Notes: 接下来，round robin调度器就交替调度两个VC

## Slide 36
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
4 pkts
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
to port 2
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
36
Notes: 接下来，round robin调度器就交替调度两个VC

## Slide 37
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
3 pkts
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
to port 1
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
37
Notes: 接下来，round robin调度器就交替调度两个VC

## Slide 38
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
2 pkts
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
to port 2
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
38
Notes: 接下来，round robin调度器就交替调度两个VC

## Slide 39
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
1 pkt
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
to port 1
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
39
Notes: 接下来，round robin调度器就交替调度两个VC

## Slide 40
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
0 pkt
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
to port 2
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
40
Notes: 接下来，round robin调度器就交替调度两个VC

## Slide 41
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
0 pkt
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
to port 1
upstream egress port
downstream ingress port
per-hop BDP
16 pkts
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
41
Notes: 接下来，round robin调度器就交替调度两个VC

## Slide 42
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
0 pkt
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
to port 1
to port 2
upstream egress port
downstream ingress port
line-rate
line-rate
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
42
Notes: 最终，把scheduler把buffer space 和 链路带宽均分给了两个VC

## Slide 43
RR Scheduler
VCj
VCi
VC queues
Immediate Buffer Allocation in InfiniFlow
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
0 pkt
Case 3: Two VCs are concurrently active without downstream congestion.
Shared buffer
to port 1
to port 2
upstream egress port
downstream ingress port
line-rate
line-rate
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
Does UABD solve all the problems?
43
Notes: 最终，把scheduler把buffer space 和 链路带宽均分给了两个VC

## Slide 44
RR Scheduler
VCj
VCi
VC queues
Q2: How to Allocate Buffer?
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
0 pkt
Case 4: Two VCs are concurrently active without downstream congestion.
with
line-rate
No downstream congestion
line-rate
downstream congestion
line-rate
Shared buffer
to port 1
to port 2
upstream egress port
downstream ingress port
Idle Buffer
Occupied Buffer
Reserved Buffer for In-flight Packets
queue ↑
44
Notes: 我们先看一下，如果不对每个VC的使用量进行限制，会发生什么问题。继续刚才的例子，假设黄色data flow的下游发生了拥塞，（click）导致排出速率只有1/4线速.由于输入速率大于排出速率，所以（click）buffer中开始堆积yellow pkts。

## Slide 45
RR Scheduler
VCj
VCi
VC queues
Q2: How to Allocate Buffer?
Idle Buffer
Data Packets
Feedback Packets*
* The feedback packets in InfiniFlow paper are denoted as Buffer Control Packets (BCPs).
credit pool
0 pkt
Occupied Buffer
Case 4: Two VCs are concurrently active without downstream congestion.
with
No downstream congestion
line-rate
line-rate
line-rate
steady state
Shared buffer
to port 1
to port 2
upstream egress port
downstream ingress port
downstream congestion
Reserved Buffer for In-flight Packets
locked
standing queue
45
Notes: 在稳态下，将呈现这样的状态，黄色流的传输速率和排出速率相等，同时将大量credit锁在了buffer里。而蓝色流虽然下游没有拥塞，但是由于RR调度策略，蓝色流的传输速率也被锁死在了1/4线速（click），造成了链路利用率不足

## Slide 46
RR Scheduler
VCj
VCi
VC queues
Q2: How to Allocate Buffer?
credit pool
0 pkt
Case 4: Two VCs are concurrently active without downstream congestion.
with
No downstream congestion
line-rate
line-rate
line-rate
steady state
Shared buffer
to port 1
to port 2
upstream egress port
downstream ingress port
downstream congestion
locked
Per-VC credit consumption must be constrained according to per-VC backlog states.
standing queue
46
Notes: 因此，仅仅根据调度策略给VC分配buffer是不够的，buffer allocation必须结合per-VC的backlog states

## Slide 47
Buffer Usage Control in InfiniFlow
Solution: Buffer Usage Control Protocol (BUCP)
Per-VC states in BUCP:
  In-flight Bytes: per-VC credit consumption
  Threshold: per-VC threshold that limits credit consumption
  Backlog: per-VC backlogged data volume in the downstream buffer
large backlog → over-credited
Data Packets
Feedback
upstream port
downstream port
Buffer
VC Queue
tighten the threshold, reduce credit consumption.
if (vc_backlog >= qmax):
threshold =
inflight_bytes – (vc_backlog – qmin)
no backlog → under-credited
Data Packets
Feedback
upstream port
downstream port
Buffer
VC Queue
relax the threshold, increase credit consumption.
if (vc_backlog < qmin):
threshold =
threshold + (qmin - vc_backlog)
BUCP aims to maintain the per-VC backlog at an extremely low but non-zero level.
47
Notes: 为了最大化链路利用率，我们提出了Buffer Usage Control Protocol。BUCP为每个VC维护了三个变量，（click）inflight bytes用来追踪每个VC的credit使用量，（click）threshold用来限制每个VC的inflight bytes，（click）backlog用来记录每个VC在downstream buffer里的backlog volume，并且每个VC的backlog会随着其feedback packets返回给上游调度器。
上游调度器如果发现VC的backlog太大，超过了静态阈值qmax，那么就会收紧threshold，来减少这个VC的credit consumption，进而避免过长的standing queue。
但是对于每个VC来说，standing queue也不是越小越好。过短的standing queue会导致，拥塞突然消失时出现链路利用率不足。
（click）因此，我们将每个VC的目标standing queue长度作为一个静态配置的非零参数qmin。当backlog小于qmin的时候，BUCP会放宽threshold，让这个VC可以使用更多的credit。 更多的detail请看论文
【这里10分钟讲完】

## Slide 48
Feature 1: Lossless Transmission
Feature 2: Decoupling Buffer Requirement with the Number of VCs
  Theoretically, a single per-hop BDP for each port.
  In practice, 3× per-hop BDP buffer per port is recommended.
Feature 3: Integrating Buffer and Rate Allocation
  RR scheduling → max-min fair rate allocation.
  Compatible with more scheduling policies
    WRR
    SP, SRTP[1]
    hierarchical scheduling[2].
Feature 4: Rate control without end-to-end CC
  Sufficient VCs → per-flow flow control[3]
[1] Behnam Montazeri et al. “Homa: a receiver-driven low-latency transport protocol using network priorities”. In SIGCOMM 2018
[2] Zhiyu Zhang et al. “vPIFO: Virtualized Packet Scheduler for Programmable Hierarchical Scheduling in High-Speed Networks”. In SIGCOMM 2024
[3] Prateesh Goyal et al. “Backpressure Flow Control”. In NSDI 2022
Features of InfiniFlow
48
Notes: 【这里11分钟讲完】

## Slide 49
InfiniFlow in Action
Notes: 预留2分钟（1.1倍速播放）

## Slide 50
Evaluations
50
Notes: 第12分钟，剩下3分钟

## Slide 51
VC Scalability Evaluation
  Per-port On-Chip Memory Requirement
  Per-port Packet Buffer Requirement
  Including the packet buffer, VC state bank, and other components
  InfiniFlow supports over 16K VCs with only 401 KB of on-chip memory per port.
  With fewer VCs, fixed overhead dominates.
  With more VCs,
  VC state overhead dominates.
Platform: U280 FPGA Accelerator Card
64 ports → 25.7 MB
51

## Slide 52
Large-Scale NS-3 Simulations
Topology: Leaf-Spine Network with 1,024 hosts
  InfiniFlow excels in average and tail FCT without relying on end-to-end rate control.
52

## Slide 53
Large-Scale NS-3 Simulations
Topology: Leaf-Spine Network with 1,024 hosts
  InfiniFlow excels in average and tail FCT without relying on end-to-end rate control.
With enough VCs, per-flow flow control becomes possible.
Is end-to-end CC still needed for rate control?
53

## Slide 54
Themis Scheduling-Aware Buffer Management for HBM-Based Hybrid Buffers NSDI 2026
54

## Slide 55: HBM-Based Hybrid Buffers
On-Chip SRAM
Off-Chip HBM
Buffer
Management
Arriving
Packets
DepartingPackets
• HBM serves as overflow buffer for packets spilled from SRAM.
• SRAM and HBM work together to achieve both high speed and large capacity.
55

## Slide 56: Existing Hybrid Buffer Designs: Poor HBM Access Patterns Reduce Effective Bandwidth
HBM accesses must satisfy two conditions to reach full rated bandwidth:
Spatial Locality: Contiguous Addresses
✓ Even data distribution across PCs and BGs → Maximum parallelism
✓ Full-row read per activation → Amortized tACT/tPRE latency
Temporal Locality: Continuous Same-Type Operations
✓ Use batches of consecutive reads or writes
✓ Avoid read/write interleaving to reduce bus turnaround overhead
However, packet-buffer access patterns inherently lack continuity
Packet arrival order ≠ Departure order
Because the scheduler determines the packet readout order, continuity of write addresses and read addresses cannot be achieved simultaneously.✗
Read-write interleaving is inevitable
Packet-arrival events are unpredictable (writes), while dequeue events continue (reads), so operation continuity cannot be guaranteed.✗
Under existing designs, measured HBM bandwidth can fall to just one-ninth of the peak bandwidth.
56

## Slide 57: Existing Hybrid Buffer Scheme – Priority Inversion
On-Chip SRAM
Off-Chip HBM
1
2
3
4
5
1
2
3
1
2
3
4
Threshold
6
8
7
9
11
10
Buffer management (length and threshold only)
The part that exceeds threshold spills into the off-chip HBM
Scheduler (based on scheduling priority)
On-Chip SRAM
Off-Chip HBM
1
2
3
1
2
3
4
6
10
8
7
9
11
Next to depart
When on-chip high-priority flows are exhausted, the scheduler must fetch packets from off-chip memory
Scheduling Priority
>
=
Traditional designs leave high-speed SRAM idle and repeatedly read and write slow HBM, failing to deliver the promised combination of speed and capacity.
Treat HBM as pure spillover space - simple but inefficient
57

## Slide 58: Themis: Scheduling-Aware Admission Control
Scheduling Priority
>
=
Themis Shared Buffer
No queue abstraction required
Traditional per-flow queue
Limit individual queue lengths
X
-----
Y
X: Arrival order
Y: Departure order, determined by the scheduler
X
X: Arrival order
1
-----
[1]
2
-----
[101]
4
-----
[102]
13
-----
[6]
16
-----
[9]
14
-----
[7]
3
-----
[2]
5
-----
[3]
6
-----
[4]
7
-----
[103]
8
-----
[105]
9
-----
[104]
10
-----
[106]
11
-----
[108]
12
-----
[5]
17
-----
[10]
1
2
3
12
13
4
7
9
5
8
10
6
11
14
15
16
17
18
Make the Buffer Manager (BM) rank-aware so that it follows the scheduler's ordering.
The next packet to depart is always kept in SRAM.
58
On-Chip SRAM
On-Chip SRAM

## Slide 59: Themis: Batched HBM Access
Actively reorganize each HBM access using contiguous addresses and a single operation type
Arriving
Packets
DepartingPackets
Scheduling Priority
>
=
1
-----
[1]
2
-----
[101]
4
-----
[102]
13
-----
[6]
16
-----
[9]
14
-----
[7]
3
-----
[2]
5
-----
[3]
15
-----
[8]
6
-----
[4]
7
-----
[103]
8
-----
[105]
9
-----
[104]
10
-----
[106]
11
-----
[108]
12
-----
[5]
17
-----
[10]
18
-----
[11]
19
-----
[110]
20
-----
[112]
21
-----
[114]
22
-----
[12]
23
-----
[116]
24
-----
[118]
25
-----
[120]
10
-----
[106]
8
-----
[105]
11
-----
[108]
Batch Write
When SRAM is nearly full, proactively spill a batch to HBM.
Reverse the packet selection logic of the scheduler.
Swap out the packet with the largest rank.
• Spatial dimension: Packets with close ranks are grouped into batches and written to contiguous addresses.
• Time dimension: Packets are written to HBM in full batches; packets are prefetched from HBM in full batches.
59

## Slide 60: Themis: Batched HBM Access
Arriving
Packets
DepartingPackets
Scheduling Priority
>
=
18
-----
[11]
19
-----
[110]
20
-----
[112]
21
-----
[114]
22
-----
[12]
23
-----
[116]
24
-----
[118]
25
-----
[120]
10
-----
[106]
8
-----
[105]
11
-----
[108]
Batch Read
Actively reorganize each HBM access using contiguous addresses and a single operation type
4
-----
[102]
7
-----
[103]
9
-----
[104]
2
-----
[101]
27
-----
[14]
26
-----
[13]
2
-----
[101]
27
-----
[14]
26
-----
[13]
When SRAM is nearly empty, proactively prefetch a batch from HBM.
Reuse scheduler packet selection logic
Swap in the packet with the smallest rank.
• Spatial dimension: Packets with close ranks are grouped into batches and written to contiguous addresses.
• Time dimension: Packets are written to HBM in full batches; packets are prefetched from HBM in full batches.
60

## Slide 61: Performance of Themis
Link Utilization
HBM Throughput
Contiguous addresses + batched access unlock effective HBM bandwidth, maximizing egress link utilization
61

## Slide 62: Performance of Themis
Higher HBM throughput lets Themis absorb larger bursts — fewer drops;
Rank-based admission keeps soon-to-depart packets on-chip — higher hit rate
Packet loss rate
On-Chip Dequeue Hit Rate
62

## Slide 63: Summary: Networks Are Evolving into AI-Native Infrastructure
The Role of Traditional Networks
The Role of Networks in the AI Era
Fundamental Shift
Goal:
Connect & Forward
Goal:
Serving AI Training / Inference / Agent Workloads
Target:
General Traffic
Target:
Periodic, Bursty AI Traffic Sensitive to Bandwidth
Method:
Passive Support for Service Demands
Method:
Traffic-Aware Adaptive Optimization
Traffic Prediction/ Engineering
NetJIT [SIGMETRICS'25]
HalfLife (EuroSys’24]
Traffic Isolation
InfiniFlow [SIGCOMM’26]
Themis [NSDI'26]
Traffic Scheduling
BMW-Tree [SIGCOMM'23] /
vPIFO [SIGCOMM'24] /
Scale-up PIFO [SIGCOMM'26]
Empowering Future-Ready Adaptive Networks
63