## Slide 1
From Prototypes to Protocols: Building the Ecosystem for In-Network Computing
Wenfei Wu
Peking University

## Slide 2: The Communication Bottleneck in Distributed Systems
Large-model training/inference and big-data analytics run at cluster scale.
Data exchange cost is non-negligible in the overall job time.
HPC clusters are single-domain, which can apply programmable dataplanes to enable end-to-end customization.
750X/2y increase of FLOPS requirement ≫ Network Increase
Idle GPU time in large-scale training

## Slide 3: In-Network Computing (INC)
Offload application functions to network devices (switches in this talk)
Accelerate applications by
  reducing traffic volume
  reducing transmission hops
  packet-granular computation-communication pipelining
  freeing host CPU/GPU for other computation
bottleneck
compute
compute
Sub-RTT
Local
Global
offload

## Slide 4: INC: offload application functions to switches
Fundamental Questions
What is the function (computation) to offload?
What is the switch hardware architecture to support the computation?
How to develop the functions to the architecture?
We are still exploring the answer. Today,
Give use cases of INC
Give intuitions (as future works) for these questions
Same Questions for Programmable Dataplanes
Network functions
PISA pipeline
P4
(new research space)

## Slide 5: The path we have taken（in 2021）
Progress
A case: offload AllReduce in multi-tenant clusters
Future work (at that time)
More applications
Resource management for more scenarios
Protocol verification

## Slide 6: The path we have taken （in 2023）
Progress
Offload AllReduce
Offload ReduceByKey
Resource management
  Job placement in INC clusters
  Runtime INC resource scheduling
Future work (at that time)
“the blank boxes”
  More applications
  Devices

## Slide 7: Today
Part 1: Effort needed by device vendors
Part 2: A new INC case for long-context inference
We first introduce the concept of INC-empower AllReduce

## Slide 8: Model Training Algorithm
Algorithm: Iterate until converge
  Compute a gradient
  Update the model
In data parallel training
  Each worker computes a gradient
  Aggregate all workers’ gradients, send the result back
  Each worker updates the model
AllReduce
  Sum up vectors across hosts and return the result to all hosts
  Also exist in tensor parallel
Laguna, et al. A Large-Scale Study of MPI Usage in Open-Source HPC Applications, SC’19
widely used in AI/HPC parallel programming

## Slide 9: Host-centric Solutions
Parameter Server (PS)
  Send all vectors to PS
  PS sums up and returns
  PS suffers from more traffic volume
Ring AllReduce
  Hosts form a ring
  Host relays intermediate vector along the ring
  Round 1: each host accumulates its own vector
  Round 2: each host store the result
  The two-round vector passing doubles the traffic volume

## Slide 10: INC Design Data Structure
Worker: chunk the gradient as a packet sequence
  Maintain a sliding window sized W to stream packets
Switch: organize the SRAM as an array of aggregators, sized N
Sapio, et al. Scaling distributed machine learning with In-Network aggregation, NSDI 2021 (KAUST, Microsoft, U Washington)
Liu, et al. In-network aggregation with transport transparency for distributed training, ASPLOS 2023 (Huawei , PKU, CityU)

## Slide 11: Workflow
Workers always sends packet in window
Switch addresses each packet to an aggregator
When switch completes an aggregation, it multicasts ACK to workers
  ACK piggybacks results
ACK advances worker’s window, and worker sends new packets
W≤N to avoid addressing errors. (necessary not sufficient)

## Slide 12
worker
0
Gradient
1
2
3
4
5
worker
0
Gradient
1
2
3
4
5
Switch
0
Agtr Array
1
Size is 2
Window Size is 2
0
1
0
1
Workflow (ideal case)

## Slide 13
0
1
2
3
4
5
0
1
2
3
4
5
0
1
1
Workflow (ideal case)
worker
Gradient
worker
Gradient
Switch
Agtr Array
Size is 2
Window Size is 2

## Slide 14
0
1
2
3
4
5
0
1
2
3
4
5
0
1
1
0
0
Workflow (ideal case)
worker
Gradient
worker
Gradient
Switch
Agtr Array
Size is 2
Window Size is 2

## Slide 15
0
1
2
3
4
5
0
1
2
3
4
5
0
1
2
2
Addressing: PSN%N
Workflow (ideal case)
worker
Gradient
worker
Gradient
Switch
Agtr Array
Size is 2
Window Size is 2

## Slide 16: Other Considerations
How to handle packet loss?
  Host applies ARQ to retransmit unACKed data packet
  Switch runs deduplication to avoid duplicate computation
How to recycle (small) switch memory for (large) messages?
  Codesign with windowing protocol: when observing inflight PSN, clear one window away
Congestion Control: work within the window constraint
Floating-Point Support: (De)quantization

## Slide 17: Evaluation Environment
Cluster
  Server*4: GeForce 3090 GPU, Mellanox CX5 100GbE NIC
  Switch*1: Tofino 1, link bandwidth 100Gbps*32
Workload: NCCLTest AllReduce
Metric: Algorithm Bandwidth
  data size / completion time

## Slide 18: Evaluation Results
With the same MTU, INC improves throughput by up to 40%
Message Size | INC | NCCL
64KB | 8.7 | 11.8
256KB | 35.2 | 16.8
1MB | 74.2 | 57.5
4MB | 80.2 | 66.0
16MB | 83.0 | 59.7
64MB | 86.2 | 61.4
256MB | 88.4 | 62.3
1GB | 87.8 | 62.6

## Slide 19: Other Considerations
Resource Management: How to allocate switch memory to jobs?
  (Job Initialization) Where to place jobs in the cluster considering INC resources?
  (Job Runtime) How to multiplex INC resources among jobs?
Lao, et al. ATP: In-network aggregation for multi-tenant learning, NSDI 2021 (Tsinghua, UW-Madison, Intel)
Zhao, et al. Enabling switch memory management for distributed training with in-network aggregation. INFOCOM 2023 (Tsinghua, PKU)
Wang, et al. Preemptive switch memory usage to accelerate training jobs with shared in-network aggregation. ICNP 2023 (PKU, HKUST)
Zhao, et al. Training job placement in clusters with statistical in-network aggregation. ASPLOS 2024 (PKU, Tsinghua)

## Slide 20: Since 2023, we try to persuade vendors to apply INC
We expect to reshape the ecosystem
From a layer architecture to a holistic one
Link
Network
Transport
Application
Comm Lib
Link
Network
Transport
Application
Comm Lib
Link
Network
host
net device
host
Device Vendor
ISP
OS Vendor
Content Provider
New Infra Vendor
Net Device
Host
Host
Application
Comm Lib
Transport
Network
Link
Application
Comm Lib
Transport
Network
Link
Comm Lib
Transport
Network
Link
The Internet Architecture
The AI Network Architecture

## Slide 21: Contents
Background
Enforce In-network Collective Communication on Ethernet
A New INC Case for Context Parallelism
Conclusion
Eth+ Consortium, In-network Collective Specification, 2024
Yuan et al., EPIC: Abstraction and Polymorphism of In-Network Collectives on Ethernet, SIGCOMM 2026 (PKU, etc.)

## Slide 22: Initial Vision Revisited
Intuition: cross-layer construction for performance gain
Too few such vendors to handle all layers.
This seldom happens
New Infrastructure Vendor
Net Device
Host
Host
Application
Comm Lib
Transport
Network
Link
Application
Comm Lib
Transport
Network
Link
Comm Lib
Transport
Network
Link
Content Provider

## Slide 23: Problem 1: Cross-layer system vs Open ecosystem
INC is cross-layer, including
  CCL, protocol stack, NIC, switch, network controller
Ethernet is an open ecosystem. INC spans econiches:
  CCL developer, protocol stack developer, NIC vendor, switch vendor, network controller developer
Concerns for a single party:
  Single party cannot complete the whole system and obtain the gain.
  Adding new functions in each functional scope is expensive.
Poor return-on-investment (ROI) deters vendors from committing resources.

## Slide 24: Problem 2: Switch vendors differ
Type-I: Some vendors build both switches and NICs (RoCE)
Type-II: Some vendors only build switches
An INC design requiring RoCE stack would prevent type-II vendors.
Many NIC vendors are building RoCE NICs.
Type-II vendors cannot follow type-I vendors’ technical approach

## Slide 25: Solution: Unified Abstraction, Polymorphic Realization
Unified Abstraction: break upstream-downstream vendor lock-in
  More choices for one vendor
Polymorphic Realization: multiple vendors for each econiche
  Reduce investment
host 1
host 2
host 3
host 4
switch 1
switch 2
switch 3
switch 4
IP1, QP1, eth0
IP2, QP2, eth2
IP3, QP3, eth0
IP4, QP4, eth3
IP5, QP5, eth1
IP6, QP6, eth2
IP12, QP12, eth3
IP11, QP11, eth1
IP8, QP8, eth2
IP10, QP10, eth3
IP7, QP7, eth0
IP9, QP9, eth0
root
leaf
leaf
leaf
leaf
edge
endpoint
(a) An aggregation tree (b) Aggregation tree on Ethernet cluster
ep1
ep5
ep2
ep3
ep4
ep6
ep7
ep8
ep9
ep10
ep11
ep12

## Slide 26: Abstraction: Components and Econiche
Preserve standard interfaces between functional scopes
  Switch, NIC, CCL, Network Controller
Host
GPU
GPU
CommLib
RoCE
NIC
Host
GPU
GPU
CommLib
RoCE
NIC
Switch
IncEngine
IncAgent
IncManager
Network
Control Plane
APPLICATION
COL. COM. Lib.
TRANSPORT
NETWORK LAYER
data IO via collectives
message IO via verbs
packet IO
Switch Vendor
Cluster Operator
OS Vendor
Content Provider
NIC Vendor

## Slide 27: Polymorphism: Mode-I (Connection Terminated)
For vendors with both switch and RoCE capability, e.g., Nvidia
Switch IncEngine reuses RoCE, add extra application-layer computation
  RoCE assemble packets as messages
  IncEngine reduces and replicates on messages
  RoCE sends messages as packets
IncEngine is like a Parameter Server
RoCE
IncEngine
LookupTable
LookupTable
(De)packetization
AggregateData
ReplicateData
Forward
HandleAck
Retransmission
ConnectionMgmt
packets
packets
msg
msg
UP_DATA
DOWN_DATA
switch workflow

## Slide 28: Mode-II: Connection Translated
For vendors with ordinary Ethernet switch capability, but no RoCE technical reserves
Minimalist design to achieve INC, with RoCE interoperability
LookupTable
CheckDuplicate
AggregateData
ReplicateData
TranslateHeader
Forward
UP_DATA
DOWN_DATA
ACK
RecycleBuffer
(a) Upward data packet (b) Downward data packet (c) Reply ACK packet (d) Reflect ACK packet
acknowleging
acknowleging
switch workflow
Legends upward data packet downward data packet ACK packet

## Slide 29: Mode-III: Connection Enhanced
Legends upward data packet downward data packet ACK packet
For vendors evolving to switch+RDMA
Add per-hop ACK and retransmission
The middle ground between Mode-I and Mode-II
timer
LookupTable
CheckDuplicate
AggregateData
ReplicateData
TranslateHeader
Forward
DATA
ACK
ReceiveAck
SendAck
Retransmission
RecycleBuffer
(a) Level-1 Aggregation (b) Level-2 Aggregation (c) Level-2 Broadcast (d) Level-1 Broadcast
switch workflow

## Slide 30: Evolvement among Modes
A vendor can evolve modes from simple to complex.
LookupTable
CheckDuplicate
AggregateData
ReplicateData
TranslateHeader
Forward
UP_DATA
DOWN_DATA
ACK
RecycleBuffer
timer
LookupTable
CheckDuplicate
AggregateData
ReplicateData
TranslateHeader
Forward
DATA
ACK
ReceiveAck
SendAck
Retransmission
RecycleBuffer
RoCE
IncEngine
LookupTable
LookupTable
(De)packetization
AggregateData
ReplicateData
Forward
HandleAck
Retransmission
ConnectionMgmt
packets
packets
msg
msg
UP_DATA
DOWN_DATA

## Slide 31: Comparison of Modes
Correctness: by model checking
Transmission Efficiency: Mode-I is message-level
Logic Complexity
Space Complexity: Mode-II needs path BDP, Mode-I/III needs hop BDP
Loss Tolerance: Mode-II’s global synchronization performs poorly
 | Mode-I | Mode-II | Mode-III
Correctness | Yes | Yes | Yes
Trans. Efficiency | Lower | Good | Good
Logic Complexity | High | Low | Medium
Space Complexity | Low | High | Low
Fault Tolerance | Good | Poor | Good
Radar Chart (Outer is better)

## Slide 32: Support Evolvability
Top vendors: Mode-I → Mode-III
  Infer to exist in Nvidia SHARP and Broadcom Tomahawk
Non-top vendors：Mode-II → Mode-III
Outer is better

## Slide 33: Advantage of Polymorphism
Enable all vendors to implement INC, breaking vendor lock-in
  Switch+RDMA vendor: Mode-I (→ Mode-III)
  Switch-only vendor: Mode-II (→ Mode-III)
Enable a single vendor to evolve from simple to complex
  Mode-II → Mode-III (→ Mode-I)
  Enable rapid product delivery, reduce investment risk
  Evolve to the best performance in long term
Clarify Concepts:
Platform Independence (Write Once, Run Anywhere): the same algorithm, compiled to heterogenous platforms.
Polymorphism: the same functionality, but different algorithms (for diverse hardware vendors)

## Slide 34: Promotion of Adoption: standardization
ETH+ Specification Release

## Slide 35: Evaluation (All parties agree)
Correctness
Performance Acceleration
Interoperability
Evolvability
Resource Manageability
Loss Tolerance
Chip Feasibility
from a chip vendor

## Slide 36: Collective Communication
INC solutions outperform non-INC solutions.
  EPIC/SwitchML/ATP > NCCL
EPIC saturates bandwidth with less CPU than SwitchML/ATP
  EPIC is hardware-offload in transmission (RoCE).

## Slide 37: Application Performance
INC accelerates communication, so it also accelerates end-to-end performance.

## Slide 38: A Model Checker for INC Protocols
Provide a language to describe
  Topology
  Node behaviors
Compile to TLA+
Run to find violations
We have not apply complex optimization yet, but simple settings find several design errors from 9 INC systems.
  E.g., in a network cache, out-of-order packets can easily cause read/write hazards.
Bai et al., Verifying In-Network Computing Systems for Design Risks, ICNP 2026 (PKU, etc.)

## Slide 39: Contents
Background
Enforce In-network Collective Communication on Ethernet
A New INC Case for Context Parallelism
Conclusion

## Slide 40: Background
Long-Context Applications：
  RAG
  Long-document understanding
  Multi-turn dialogue memory
Long-context increases:
  KV cache memory
  Attention computation
  Inter-GPU communication
CP：Split the sequence across GPUs, sharing KV cache via communication
Wan et al., Turbo: Efficiently Serving Long-Context Large Language Models with In-Network Aggregation, SIGCOMM 2026 (SEU, PKU, Tencent, etc.)

## Slide 41: Algorithm
The current iteration has tokens 1, …s, transformed to KV cache
  k1, …, ks and v1, …, vs
  Token n’s query qs
Compute attention
Generate the next token s+1

## Slide 42: Existing Solutions & Their Limitations in Decoding
Pass-KV
  Ring： KV blocks are circulated among workers and sent to the master
  Limitation:
    High communication volume and network demand
    Decode latency increases with the number of workers
Pass-Q
  P2p：The master broadcasts queries and aggregates partial attention results
  Limitation:
    Reduces link traffic, but creates incast and reduce bottlenecks

## Slide 43: INC Solution (Turbo)
Broadcast q by the switch
Reduce “partial attention” ai by the switch

## Slide 44: The Attention Computation
Broadcast q by the switch
  Each worker generates partial attention ai and weight wi
Reduce “partial attention” ai by the switch
On switch, ai arrives consecutively, so we incrementally compute a

## Slide 45: Challenge 1: Switch Programmability Limitation
We cannot perform multiplication and division
We build lookup tables to compute the equation
  Precompute all and look up in the runtime
  To get new
Compress table size
  Quantize attention a as INT8
  Use log w to represent w

## Slide 46: Challenge 2: Switch Memory Access Limitation
RMT pipeline constraints
  Full update logic does not fit in one stage
  Cross-stage state read/write is not allowed
Rolling-forward state update
  Split updates across stages
  Shift consecutive packets by two stages
  Read the previous state at the correct stage

## Slide 47: Evaluation
Testbed
  4 nodes × 2 RTX 3090 GPUs
  100 Gbps NIC
  Tofino2 programmable switch
  LLAMA-2 7B + ShareGPT
Large-scale Evaluation
  16 nodes, 200 Gbps RoCEv2
  ToR and Spine-Leaf topologies
  LLAMA-2 7B and GPT-3 175B
  up to 32 concurrent tasks

## Slide 48: Testbed Results
Turbo scales better as the number of nodes increases
TPOT：Time Per Output Token
Up to 37%
lower decoding latency
at 8 nodes vs. Pass-KV ring

## Slide 49: Large-scale Results
Turbo reduces master traffic while maintaining lower TPOT

## Slide 50: Contents
Background
Enforce In-network Collective Communication on Ethernet
A New INC Case for Context Parallelism
Conclusion

## Slide 51: Research Roadmap
Network Devices
Raise performance ceiling
Communication Layer
Make INC easy for developer to use
Machine Learning
Data Analytics
Storage
Accelerate more applications
Runtime Mgmt
Use resources efficiently
Tools for Develop-ment
Ensure correct design
Tech stack

## Slide 52: Conclusion
Years of effort shows that INC is promising to accelerate distributed systems.
EPIC enables the fragmented Ethernet ecosystem to construct cross-layer system.
  INC AllReduce algorithm is well-studied.
  Apply “unified abstraction, polymorphic realization” to bridge the fragmented ecosystem
Turbo shows another use case of INC: Context Parallelism
  It builds a new ScalingReduce primitive
  It overcomes limitations of programmable switches.

## Slide 53: Future Work
Short-term goals
  For existing INC use cases, deploy them and build better management policy.
  Discover more use cases
  Build better switch microarchitectures (isolate INC and packet forwarding)
Long-term goals: Performant infrastructure to enable scientific findings
  Approach: make network the accelerator for distributed applications.
    Like that GPU is the accelerator of servers.
  What is the function (computation) to offload?
    It seems to be stream processing (data units traversing the processor)
  What is the switch hardware architecture to support the computation?
    Pipeline architecture seems reasonable (customize the ISA).
  How to develop the functions to the architecture?
    Thinking about this, extended-P4? Functional Programming?

## Slide 54: Q&A
Wenfei Wu, Assistant Professor
Focus on distributed systems and computer networking
INC workgroup leader of Eth+ Consortium
Research about INC
  INC acceleration system, to promote system execution efficiency.
  INC management, to promote cluster resource efficiency.
  INC environment adaptation, to enable agile deployment.
ASPLOS’23 Distinguished Paper
NSDI’21 Best Paper
CCPC’24 Best Academic Paper